## Slide 1
Investigation into potential risks associated with the use of treated municipal sludge on agricultural land
Healy, M.G., Fenton, O., Cummins, E., Clarke, R., Peyton, D.P., Fleming, G.T.A., Wall, D., Morrison, L., and Cormican, M.

## Slide 2
Background
Wastewater in
Clean water out
Sludge generated

## Slide 3
Background
Sewage sludge destination routes in Ireland in 2014*
 | Agriculture | Composting | Landfill | Other | Total
Quantity (tonnes dry solids) | 42,483 (79.3%) | 9,266 (17.3%) | 361 (0.7%) | 1,433 (2.7%) | 53,543
*EPA. 2015. Urban Waste Water Treatment in 2014.
http://www.epa.ie/pubs/reports/water/wastewater/2014%20waste%20water%20report_web.pdf

## Slide 4
Background
http://www.bordbia.ie/industry/farmers/quality/SDQASDocuments/SustainableDairyAssuranceScheme-ProducerStandard.pdf

## Slide 5
Background
Benefits of recycling treated sludge (‘biosolids’) to grassland:
  May be used as a soil conditioner, improving physical, chemical and biological properties
  May reduce the possibility of soil erosion
  A cheap alternative to commercial fertiliser
© Scanship Bio-sludge Treatment
© The James Hutton Institute

## Slide 6
Background
Drawbacks of recycling biosolids to grassland:
  Nutrient, metal and suspended sediment losses may occur
  Presence of ‘emerging contaminants’, such as pharmaceuticals, microplastics, etc.
  Presence of human enteric pathogens, as complete sterilisation is difficult to achieve
  Metals may accumulate in soils and crops after repeated applications
© Scanship Bio-sludge Treatment
© The James Hutton Institute

## Slide 7
To characterize the metal and pharmaceutical concentrations in treated municipal sludge in Ireland.
The measure the surface runoff of nutrients, solids, microbial matter, pharmaceuticals and metals following land application.
To measure the update of metals by vegetation (ryegrass).
Research aims

## Slide 8
To characterize the metal and pharmaceutical concentrations in treated municipal sludge in Ireland.
Research aims

## Slide 9
Methodology – Metal characterisation
Treated sludge was collected from 16 wastewater treatment plants (WWTPs) with population equivalents (PE) ranging up to approximately 2.3 million.
Metals analysed using a handheld X-ray fluorescence (XRF) analyser
Metals examined: Cadmium (Cd), chromium (Cr), copper (Cu), iron (Fe), mercury (Hg), molybdenum (Mo), nickel (Ni), lead (Pb), antimony (Sb), selenium (Se), tin (Sn), and zinc (Zn)

## Slide 10
Methodology – Pharmaceutical characterisation
Treated sludge was collected from 16 wastewater treatment plants (WWTPs) with population equivalents (PE) ranging up to approximately 2.3 million.
Pharmacuetical analysed using mass spectrometry
Pharmaceuticals examined: Triclosan and Triclocarban

## Slide 11
Methodology
Three types of biosolids, were examined:
  anaerobically digested (AD)
  lime stabilized (LS)
  thermally dried (TD)

## Slide 12
Results
Characterization of biosolids from 16 WWTPs
Limit values for metal concentrations in sludge for use in agriculture
Healy et al. 2016. Waste Manage. 48: 404-8

## Slide 13
Metal | Anaerobic digestion |  | Lime stabilisation |  | Thermal drying | 
 | Mean | SD | Mean | SD | Mean | SD
As | <LOD |  | <LOD |  | <LOD | 
Se | 3 | 2 | 3 | 1 | 2 | 1
Sr | 162 | 61 | 183 | 75 | 114 | 36
Mo | 5 | 2 | 4 | 1 | 5 | 1
Ag | 11 | 2 | 11 | 3 | 8 | 3
Sn | 55 | 57 | 23 | 4 | 23 | 5
Sb | 20 | 5 | 17 | 3 | 17 | 4
Cr | 51 | 43 | 25 | 15 | 16 | 12
Concentrations (mg kg-1) of unlegislated metals (in the EU) in the treated sludge
Antimony (Sb) is substantially higher than in non-polluted soils (0.53 mg kg-1)
Results
Characterization of biosolids from 16 WWTPs
Healy et al. 2016. Waste Manage. 48: 404-8

## Slide 14
Results
Presence of pharmaceuticals in 16 WWTPs
Healy et al. 2016. Waste Manage. 48: 404-8

## Slide 15
Addendum to study
Small particles of plastic, called ‘microplastics’, have also been found on sludge particles.
These may carry contaminants that may attach to their surface.
McMahon et al. 2016. In press.

## Slide 16
To characterize the metal concentrations in treated municipal sludge in Ireland.
The measure the surface runoff of nutrients, solids, microbial matter, pharmaceuticals and metals following land application.
To measure the update of metals by vegetation (ryegrass).
Research aims

## Slide 17
The measure the surface runoff of nutrients, solids, microbial matter, pharmaceuticals and metals following land application.
Research aims

## Slide 18
Aims
To quantify losses of:
  nutrients
  metals
  microbes (total and faecal coliforms)
  anti-microbial agents, triclosan and triclocarbon
in runoff from micro-plots (n=5) at time intervals of 24, 48 and 360 hr following application of three types of biosolids
  Thermally dried
  Anaerobically digested
  Lime stabilised
applied at the legal application rate.
© Scanship Bio-sludge Treatment
© The James Hutton Institute
Runoff was also compared to runoff from dairy cattle slurry, applied at the same rate.

## Slide 19
Methodology
Plot isolated using PVC sheeting (50 mm below soil surface)
Rainfall simulators used to apply rain 24, 48, 360 hr after application date
Target Intensity 10.5 mm hr-1

## Slide 20
0.4 m
0.9 m

## Slide 21
Results
Phosphorus loss in runoff
RS1 = 24 hr after application
RS2 = 48 hr after application
RS3 = 360 hr after application
Peyton et al. 2016. Sci. Tot. Env. 548: 218-29

## Slide 22
Results
Phosphorus loss in runoff
RS1 = 24 hr after application
RS2 = 48 hr after application
RS3 = 360 hr after application
Peyton et al. 2016. Sci. Tot. Env. 548: 218-29

## Slide 23
Results
Nitrogen loss in runoff
RS1 = 24 hr after application
RS2 = 48 hr after application
RS3 = 360 hr after application
Peyton et al. 2016. Sci. Tot. Env. 548: 218-29

## Slide 24
Results
Metal loss in runoff
Regulated parameter | Surface water limit (µg L-1)* | Runoff in excess of surface water limit
Nickel (Ni) | None | n/a
Copper (Cu) | 20 | Yes
Zinc (Zn) | 500 | No
Cadmium (Cd) | 1 | No
Lead (Pb) | 50 | No
Chromium (Cr) | 50 | No
Peyton et al. 2016. Sci. Tot. Env. 548: 218-29
* S.L. 549.21

## Slide 25
Results
Metal loss in runoff
Cadmium Chromium
Peyton et al. 2016. Sci. Tot. Env. 548: 218-29

## Slide 26
Results
Total and faecal coliform loss in runoff
Peyton et al. 2016. Sci. Tot. Env. 548: 218-29

## Slide 27
Results
Pharmaceutical loss in runoff
 | Triclosan |  |  |  |  | Triclocarban |  |  | 
 | Influent | 1 d | 2 d | 15 d |  | Influent | 1 d | 2 d | 15 d
 | µg g-1 | µg L-1 |  |  |  | µg g-1 | µg L-1 |  | 
TD | 4.9 | <LOD | <LOD | <LOD |  | 0.05 | <LOD | <LOD | 0.01
LS |  | <LOD | <LOD | <LOD |  |  | 0.02 | <LOD | <LOD
AD | 0.27 | <LOD | <LOD | <LOD |  | <LOD | <LOD | <LOD | <LOD

## Slide 28
To characterize the metal concentrations in treated municipal sludge in Ireland.
The measure the surface runoff of nutrients, solids, microbial matter, pharmaceuticals and metals following land application.
To measure the update of metals by vegetation (ryegrass).
Research aims

## Slide 29
To measure the update of metals by vegetation (ryegrass).
Research aims

## Slide 30
Best landspreading practices
Guidelines state that ‘no animal fodder, including kale, food beet or silage, may be harvested until at least three weeks after application of biosolids, and livestock should not be turned out to pasture which has been fertilised with biosolids until three to six weeks after the date of application’.
Fehily Timoney and Company (1999) Codes of good practice for the use of biosolids in agriculture - guidelines for farmers. http://www.environ.ie/en/Publications/Environment/Water/FileDownLoad,17228,en.pdf

## Slide 31
Best landspreading practices
To investigate this regulation, we applied three types of biosolids to grassland (ryegrass) plots and measured the metal uptake over a period of up to 18 weeks.
The treatments were:
Anaerobically digested biosolids
Lime stabilised biosolids
Thermally dried biosolids
A study control (grass without biosolids)

## Slide 32
Best landspreading practices
All legislated metals (Cr, Cu, Pb, Ni, Zn, Cd) had similar concentrations to study control and reduced in concentration over time.

## Slide 33
Conclusions of metal uptake by plant study.
There was no statistically significant difference between shoot metal concentration of ryegrass in biosolids-amended plots and unamended (control plots).
On the basis of the parameters measured, it would appear the guidelines are overly strict.

## Slide 34
Overall conclusions
On the basis of these micro-plot experiments:
Biosolids application to agricultural land are no more dangerous than applications of agricultural slurry.
Regulations governing the time between biosolids application and animal foraging on the same plot would seem to be overly strict.
An important caveat…
Pharmaceuticals and other emerging contaminants, which may be present in sewage sludge, may be inadvertently applied to land and build up in the soil after continued application.

## Slide 35
Acknowledgement
The authors wish to acknowledge funding from the Irish EPA (Project reference number 2012-EH-MS-13) and the Department of Communications, Energy and Natural Resources under the National Geoscience Programme 2007 – 2013 (Griffiths Award).
Email: mark.healy@nuigalway.ie
Web: nuigalway.ie/gene/